## Slide 1
Introduction to the DE0 Board
Prof. Taeweon Suh
Computer Science & Engineering
Korea University
COSE221, COMP211 Computer Logic Design

## Slide 2: DE0 Board
7 Segments
Serial Port
FPGA
(Cyclone-III)
LEDs
Push Buttons
Switches

## Slide 3: More Detailed Info

## Slide 4: DE0 Board Connections

## Slide 5: Push Buttons
Push button provides
  Low (0 V) when pressed
  High (3.3V) when NOT pressed

## Slide 6: Switches
Switch provides
  Low (0 V) when the switch is in the DOWN position (closest to the edge of the board)
  High (3.3 V) when the switch is in the UP position

## Slide 7: 7 Segments
To light up a segment, provide a low level
To turn off a segment, provide a high level

## Slide 8: LEDs
10 green LEDs on the board
To turn on the LED, provide a high level
To turn off the LED, provide a low level

## Slide 9: Pin Assignment
Let’s use the same names in our design as listed in the manual
  Then, we don’t have to manually assign inputs and output in our design to the FPGA pins
  Just import the pin assignment file (excel file) from Quartus-II, which is linked in the class web

## Slide 10: Lab 1 Getting Started
BUTTON[1]
BUTTON[0]
LEDG[9]